## Slide 1
2 + 2 = ?
ALU
(arithmetic logic unit)

## Slide 2
ALU + MEMORY
(5 + 3) × (7 + 2)
calculator
M+
MR
8
stash
memory
8
stash an intermediate, recall it later — already half a CPU

## Slide 3
WHAT MAKES A CPU
Program
memory
Program
counter
Decoder
Clock
ALU
RAM
fetch → decode → execute → advance

## Slide 4
THE VON NEUMANN ARCHITECTURE
MEMORY
program
data
CPU
reads its own instructions
one memory. programs and data both live there.

## Slide 5
TODAY: EVERY LAYER
caesar.thcc
source
parse
AST
tree
codegen + link
.asm / .hex
machine code
load
THMM
hardware
run
RAM cells
result
human-readable code ↓ electrons (well, simulated)

## Slide 6
BY THE END, THIS CPU WILL READ THIS
JCJUM JS DCAFE

## Slide 7
MEET THMM
THMM
ACC
ALU
RAM[256]
9 instructions
loadm addr load mem → acc
loadn imm load literal → acc
store addr acc → mem
addm addr acc += mem
addn imm acc += literal
subm addr acc -= mem
mulm addr acc *= mem
divm addr acc /= mem
halt stop
16-bit · 256 cells · 9 instructions · ~200 lines of Python

## Slide 8
THE EASY CASE
c = a + b
loadm a
addm b
store c
accumulator
?
start
a
loadm a
a+b
addm b
every expression's code leaves its value in the accumulator

## Slide 9
THE PAIN
(a + b) × (c + d)
loadm a
addm b
store t0 ← stash
loadm c
addm d
store t1 ← stash
loadm t0 ← reload
mulm t1
memory
acc
a+b → ... → answer
t0
a + b
t1
c + d
now imagine 80 of these — by hand — without bugs

## Slide 10
A REAL PROGRAM
// 3-4-5 right triangle. Expected: hyp_sq = 25.
int a = 4;
int b = 3;
int hyp_sq = a * a + b * b;
3
4
?
three lines. compile, run, read RAM[16].

## Slide 11
WHAT WE GOT
16
9
25
the square on the hypotenuse
sqrt
not in the instruction set
we can compute the area. the side is not our problem.

## Slide 12
STEP 1 · PARSE → TREE
int hyp_sq = a * a + b * b ;
+
×
×
a
a
b
b
expressions nest, so they're trees

## Slide 13
HASKELL · THE ABSTRACT SYNTAX TREE
data Expr
= Lit Int
| Var String
| BinOp Op Expr Expr
data Op = Add | Sub | Mul | Div
three lines define the entire expression language

## Slide 14
HASKELL · PRECEDENCE IS DATA
operatorTable =
[ [ binaryL "*" Mul, binaryL "/" Div ] ← binds tighter
, [ binaryL "+" Add, binaryL "-" Sub ] ← binds looser
]
row order = precedence. grammar as data, not code.

## Slide 15
CODEGEN · EASY CASE
×
a
a
loadm a
mulm a
accumulator
?
start
a
loadm a
a²
mulm a
leaves emit one instruction. the contract: value lives in the accumulator.

## Slide 16
CODEGEN · THE TEMP DANCE
+
×
×
a
a
b
b
loadm a
mulm a
store t0 ← stash a²
loadm b
mulm b
store t1 ← stash b²
loadm t0 ← reload
addm t1
store hyp_sq
acc
t0
t1
stash the left, compute the right, recombine

## Slide 17
HASKELL · THE CODEGEN FUNCTION
genExpr _ (Lit n) = ... -- emit loadn
genExpr vars (Var x) = ... -- emit loadm
genExpr vars (BinOp op l r) = ... -- recurse: l, then r, combine
pattern-matches on tree shape. leaves emit; branches recurse.

## Slide 18
STEP 3 · LINK · NAMES → ADDRESSES
before
loadm a
mulm a
store t0
loadm b
mulm b
store t1
loadm t0
addm t1
store hyp_sq
halt
after
4: loadm 14
5: mulm 14
6: store 17
7: loadm 15
8: mulm 15
9: store 18
10: loadm 17
11: addm 18
12: store 16
13: halt
address table
a
→
14
b
→
15
hyp_sq
→
16
t0
→
17
t1
→
18

## Slide 19
SAME PROGRAM. FOUR WAYS.
source (.thcc)
int a = 4;
int b = 3;
int hyp_sq = a * a + b * b;
AST
+
×
×
a
a
b
b
assembly (.asm)
0: loadn 4
1: store 14
2: loadn 3
3: store 15
4: loadm 14
5: mulm 14
6: store 17
7: loadm 15
8: mulm 15
9: store 18
10: loadm 17
11: addm 18
12: store 16
13: halt
machine code (.hex / .bits)
0x3004 0011 0000 0000 0100
0x400E 0100 0000 0000 1110
0x3003 0011 0000 0000 0011
0x400F 0100 0000 0000 1111
0x200E 0010 0000 0000 1110
0xB00E 1011 0000 0000 1110
0x4011 0100 0000 0001 0001
0x200F 0010 0000 0000 1111
0xB00F 1011 0000 0000 1111
0x4012 0100 0000 0001 0010
0x2011 0010 0000 0001 0001
0x7012 0111 0000 0001 0010
0x4010 0100 0000 0001 0000
0x1000 0001 0000 0000 0000

## Slide 20
CAESAR CIPHER
Used in Roman military dispatches.
~50 BC
Each letter shifted by a fixed key.
shift 3: A → D, B → E, C → F
Trivially broken by frequency analysis.
but it's the ancestor of every cipher since
ROT13 (shift 13) is still used today.
spoiler tags on the internet
A
N
G
T
shift
3

## Slide 21
EVERY TIME YOU PRESS RUN
caesar.thcc
source
parse
AST
tree
codegen + link
.asm / .hex
machine code
load
THMM
hardware
run
RAM cells
result
parse · generate · link · execute